## Slide 1
Air Force Weather Agency
AFWA Sources
Of
Land States
George Gayno – AFWA
Fei Chen – NCAR
Ken Mitchell and Mike Ek – NCEP
Wednesday June 18, 2003
Notes: 3
1

## Slide 2: AGRMET
AGRMET – Agriculture Meteorology Model.
Global land data assimilation system.
  Hourly analyses at 48 km resolution.
  4 soil layers – 0-10, 10-40, 40-100, 100-200 cm.
  1 atmospheric layer.
Analyzed fields include:
  Soil moisture (liquid/frozen).
  Soil temperature.
  Evapotranspiration.
  Short and longwave radiation.

## Slide 3: AGRMET
Continuously cycled.
Runs “uncoupled” or “off-line.”
The soil hydrology physics are forced with analyses of
  Shelter height temperature, relative humidity and wind speed.
  Short and longwave radiation.
  Precipitation.

## Slide 4
AGRMET
Much work has been done to make AGRMET fields compatible with WRF.
  Uses Noah soil hydrology physics (Ek et. al, 2003)
  Same vegetation type database (NCAR/USGS).
  Same soil type database (STATSGO/FAO).
  Same lower thermal boundary condition (ISLSCP).
  Same greenness fraction database (Gutman and Ignatov)
Notes: 3
1

## Slide 5
Recent Model Changes
New lower thermal boundary condition file – 8/8/02.
  One-degree ISLSCP data.
  Applied at 8 meters depth instead of 3 meters.
  Twelve month parallel “spin up” period.
  Replaced four-degree data set.
Additional GFS levels used in shelter height analysis – 8/29/02
  Thirteen levels between 1000 and 500 mb.
  Previously used only 1000, 850 and 700 mb.
Implemented NCEP improved (Ek) snow albedo database – 10/18/02.
  Extended Robinson and Kukla (1985) database globally.
Notes: 3
1

## Slide 6
GRIB Data
AGRMET runs on two polar stereographic grids.
  Not convenient for use in WRF.
Therefore, interpolate data to a global lat/lon grid.
  Half degree resolution.
  Use nearest neighbor approach to avoid interpolation across different soil types.
  All fields needed to run WRF.
  Bitmap section to save disk space/bandwidth.
Data available to WG-14 users in real-time.
  Thirty day restriction to general public.
Two year archive at AFWA available for research.
  Two (00/12z) or four files (00/06/12/18z) per day.
Notes: 3
1

## Slide 7: GRIB Data
NCAR archive – started October 2002.
  NCAR’s mass storage under directory: /MESOUSER/DATASETS/AGRMET
  Only data older than thirty days.
  Data format handbook available at: http://www.mmm.ucar.edu/mm5/mm5v3/data/agrmet.html

## Slide 8
Recent Data Changes
Units of canopy water changed to mm – May 29, 2003.
Added instantaneous skin temperature – Nov 7, 2002.
Added numerous fields – May 30, 2002.
Liquid volum. soil moisture | Total volum. soil moisture
Average albedo | Greenness fraction
Avg. sensible heat flux | Avg. latent heat flux
Vegetation type | Snow depth
Baseflow runoff | Surface runoff
Avg. downward solar | Avg. downward IR
Avg. ground heat flux | Avg. skin temperature
Notes: 3
1

## Slide 9
QUESTIONS?