## Slide 1: Implementation and preliminary test of the unified Noah LSM in WRF
F. Chen, M. Tewari, W. Wang, J. Dudhia, NCAR
K. Mitchell, M. Ek, NCEP
G. Gayno, J. Wegiel, AFWA
In collaboration with: FSL/NCAR WRF/SI/Real groups
Why we need land surface models
New capabilities of the unified Noah LSM package
Preliminary test results

## Slide 2: Need for land surface models
The lower boundary is the only physical boundary for atmospheric models
The basic function of a land surface model is to provide accurate surface sensible, latent heat fluxes, and surface skin temperature as lower boundary conditions
LSM becomes increasingly important:
  More complex PBL schemes are sensitive to surface fluxes and cloud/cumulus schemes are sensitive to the PBL structures
  NWP models increase their grid-spacing (1-km and sub 1-km). Need to capture mesoscale circulations forced by surface variability in albedo, soil moisture/temperature, landuse, and snow
  Seven LSM related presentations at 2003 MM5 and WRF workshop
Not a simple task: tremendous land surface variability and complex land surface/hydrology processes
Initialization of soil moisture/temperature is a challenge

## Slide 3: Major accomplishments in WRF WG14 (land surface modeling) to embrace the WRF Test Plan
FSL/NCAR SI/Real team: New SI/Real to add new surface fields and to read various land data sources in GRIB format
Develop and evaluate the unified Noah LSM: a collaborative effort among NCEP, NCAR, AFWA, and universities
NCAR LSM team: tested and implemented the unified Noah LSM in WRF-mass and in MM5 V3.6.
FSL LSM team: implemented the RUC LSM in WRF-Mass
NCEP, AFWA, FSL: developed GRIB tables for defining new land surface variables/parameters and modified their GRIB

## Slide 4: New capabilities of the unified Noah LSM
Improved Physics
  Frozen-ground physics
  Patchy snow cover, time-varying snow density and snow roughness length
  Soil heat flux treatment under snow pack
  Modified soil thermal conductivity
Additional background fields
  Monthly global climatology albedo (0.15 degree)
  Global maximum snow albedo database
Import various sources of soil data
  NCEP Eta/EDAS (40-km): 4-layer soil moisture and temperature
  NCEP AVN/GFS/Reanalysis: 2-layer soil data
  AFWA AGRMET: global land data assimilation system (47-km); 4-layer soil data
  NCEP NLDAS: North-American land data assimilation system (1/8 degree); 4-layer soil data
  Able to read important soil and landuse parameters required by the community in addition to basic land state variables

## Slide 5: Comparison of AGRMET (47-km) and EDAS (40-km) soil moisture for soil layer 1 and 2 valid at 12Z May 31 2002
at 5 cm
at 25 cm

## Slide 6: Nine IHOP/NCAR Surface, soil, and vegetation stations. Plus one (site 10) from CU
ABLE Network
OK Mesonet
Western Leg
Sites 1, 2, 3
CU station 10
Central Leg
Sites 4, 5, 6
Eastern Leg
Sites 7, 8, 9

## Slide 7
WRF/ Unified Noah coupled model verification
(with 10-km grid spacing)
IHOP case
31 May 2002
Clear sky day
Sites 1, 2, 3
Sites 7, 8, 9

## Slide 8
WRF/ Noah coupled model (10-km) verification
Latent heat fluxes at sites 1, 2, 3 for 31 May 2002
Using AGRMET soil conditions
Using EDAS
soil conditions

## Slide 9
WRF/ Noah coupled model (10-km) verification
Latent heat fluxes at sites 7, 8, 9 31 May 2002
Using AGRMET soil conditions
Using EDAS soil conditions

## Slide 10
The unified Noah LSM significantly improved the precipitation score
compared to its predecessor OSULSM
Realtime 22-km CONUS 12Z Cycle initialized from 40-km EDAS
12 day 12-36 h
forecasted rainfall
from 15 to 31 May 2003 verified on #212 grid
Unified Noah LSM
OSULSM
Precip scores available
at NSSL website

## Slide 11
WRF/Noah Snow forecast capability
Snow Storm Case 18 March 2003
24-h snow water equivalent change valid at 06Z 19 March
Analysis: 24-h SWE change valid at 06Z 19 March
Snow melted
too quickly in
the OSULSM
accumulation
melt/sublimation

## Slide 12: Summary and Future Work
Compared to IHOP data, the WRF/Noah seems able to simulate the small scale variability, but the results are sensitive to the sources of initial soil moisture
Need to evaluate different sources of soil data (EDAS, NLDAS, AGRMET) and their impacts on WRF coupled results
Unified Noah LSM will be released with the ‘research version’ of WRF
Coupling a simple urban-canopy model to Noah
(Dr. Kusaka from CRIEPI)
Further changes in snow physics (NCEP)
Improve soil hydrology and canopy resistance

## Slide 13
30-meter resolution
USGS NLDC
Landuse data
for the Houston Area
detailed
urban
classification

## Slide 14
Unified Noah LSM (Pan and Mahrt, 1987; Chen et al., 1997; Chen and Dudhia, 2001; Ek et al. 2003)
Gravitational Flow
Internal Soil
Moisture Flux
Internal Soil
Heat Flux
Soil Heat Flux
Precipitation
Condensation
on
bare
soil
on
vegetation
Soil Moisture Flux
Runoff
Transpiration
Interflow
Canopy Water
Evaporation
Direct Soil
Evaporation
Turbulent Heat Flux to/from
Snowpack/Soil/Plant Canopy
Evaporation
from Open Water
Deposition/
Sublimation
to/from
snowpack
 = 10 cm
 = 30 cm
 = 60 cm
 = 100 cm
Snowmelt

## Slide 15
WRF/ Noah coupled model (10-km) verification
Sensible heat fluxes at sites 1, 2, 3
Using AGRMET soil conditions
Using EDAS soil conditions

## Slide 16
WRF/ Noah coupled model (10-km) verification
Sensible heat fluxes at sites 7, 8, 9
Using AGRMET soil conditions
Using EDAS soil conditions