## Slide 1: Continued Application and Development of a High-Resolution Land Data Assimilation System (HRLDAS)
Kevin W. Manning, Fei Chen
-- Mukul Tewari
-- Dave Gochis
-- Andrea Hahmann
National Center for Atmospheric Research
Boulder, CO
Notes: Today I’ll be talking about HRLDAS, our High-Resolution Land Data Assimilation System we’ve been developing in recent years.
I want to acknowledge my co-authors up front:
- Fei Chen heads up this HRLDAS effort here at NCAR,
- Dave Gochis has been implementing the water routing scheme I’ll discuss later,
- Mukul Tewari implemented the Urban modifications and has taken care of some of the real-time experiments with HRLDAS,
- and Andrea Hahmann and Yubao Liu have implemented HRLDAS in the ATEC RTFDDA.
We’ve talked about HRLDAS in the past in various venues, so I won’t go into details on it. But I will give a brief overview of HRLDAS, and then I’ll concentrate on recent applications and development.

## Slide 2: The Problem
Atmospheric models running LSM physics require initial conditions of soil temperature and moisture
No routine observations of soil conditions are performed on the large scale
  Isolated mesonets
  Satellite uncertainties
Initializing soil conditions for one model from analyses generated in other modeling and assimilation systems can lead to serious imbalances in the soil fields, due to
  Differing representations of soil textures, vegetation types, etc.
  Horizontal interpolation
  Differing representations of land-surface physical processes
Notes: The problem that HRLDAS addresses is the initialization of soil fields for atmospheric models using LSM physics.
No routine observations of soil conditions are performed on the large scale. Isolated mesonets may take these measurements, but it usually for a limited area. Derivation of these fields from satellite measurements is difficult and uncertain.
What is often done is to initialize soil conditions from some other model’s assimilation system. But this can lead to serious imbalances in the soil fields.
These come about from
- Soil textures and vegetation types may differ between models
- Horizontal interpolation may seriously mis-characterize the conditions at some particular point
- Land-surface physics packages may be different from one model to another.

## Slide 3: HRLDAS
Noah LSM run in a standalone, decoupled configuration (i.e., no atmospheric model), driven by hourly analyses of precip, radiation, and atmospheric fields
On the same model grids as an intended WRF or MM5 simulation
  “Spun-up” initial soil conditions for coupled model
  No mismatch in soil or vegetation categories or physical parameters between models
  No horizontal interpolation necessary
  Uses same LSM physics as WRF Noah LSM in order to minimize imbalances at model initialization
Spin-up on the order of a few months to a year may be necessary
  Depends greatly on soil texture
  CPU time really is not much – the bigger issue is simply managing the data
Notes: We’ve developed HRLDAS in an attempt to address this problem.
In HRLDAS, we run the Noah LSM on a horizontal grid, decoupled from an atmospheric model, and forced by 2d analyses of precipitation, radiation, and atmospheric fields.
- We run this on the same model grids as a subsequent atmospheric model simulation, for several months to a year or more.
This gives us fine-scale initial fields of soil conditions, particularly temperature and moisture, suitable to initialize a WRF/Noah coupled model.
There are several benefits of this method.
- the soil conditions are in “spun-up” state, already in near-balance ….
- There is no mismatch between soil or vegetation categories or physical parameters between the model used to generate soil categories and the model used for atmospheric simulations
- No horizontal interpolation necessary between model used to generate soil categories and the model used for atmospheric simulations
- Same LSM physics between the model used to generate soil categories and the model used for atmospheric simulations

## Slide 4: Goal: Assimilate observations into LSM to provide high-resolution land state variables for coupled models
4-km HRLDAS surface soil moisture
Notes: This slide illustrates the flow of data into HRLDAS, and out of HRLDAS into WRF:
Input to HRLDAS are
- maps describing soil and vegetation parameters (constant)
- variable land-cover information of snow, vegetation cover, and leaf area index
- forcing fields of precipitation, radiation, and atmospheric conditions
Fields from HRLDAS are transferred to the WRF initial conditions file:
- Soil moisture
- Soil temperature
- Snow cover
- Canopy water
And finally, the WRF model is run with the Noah LSM option

## Slide 5: Recent applications
IHOP studies
DWFE
Summer ARW-WRF experiments at NCAR
ATEC RTFDDA
Notes: From that very high-level overview, we’ll turn now to discussing a few recent applications of HRLDAS.

## Slide 6: Recent applications
IHOP convective studies
EDAS soil moisture 0 – 10 cm
12 Z 09 June 2002
HRLDAS soil moisture 0 – 10 cm
Notes: The IHOP experiment ran in 2002 over the central U.S. We’ve been doing some convective initiation studies at NCAR; Fei Chen, Stan Trier, and myself.
The suspicion is that gradients in surface fluxes generated by soil conditions may help to initiate convection.
To support our convection initiation studies, we’ve run HRLDAS over the central US on a 4-km grid for 18 months, from January 2001.
This slide shows initial soil moisture conditions for two WRF runs, on the left is initial conditions from EDAS, on the right is initial conditions generated by HRLDAS.
The HRLDAS conditions show much more surface heterogeneity than the EDAS conditions, generated by variations in soil texture and vegetation categories and recent precipitation.
One other obvious difference is that HRLDAS has considerably drier conditions overall. We’re a little concerned about this; we suspect it is a little *too* dry. We’re looking into using a different precipitation analyses that may give more rainfall.

## Slide 7: Recent applications
Snow depth (m)
Snow cover
24-h accumulated runoff
Volumetric total soil moisture (liquid+ice)
Volumetric soil ice (frozen soil)
DWFE – DTC Winter Forecast Experiment
Notes: The DTC ran a winter forecast experiment this year, and HRLDAS was used to initialize soil conditions for one set of forecasts. These runs were on a 5-km CONUS grid. Mukul Tewari kept HRLDAS going for this experiment.
This slide is from one of these cases, in March 2005, demonstrating the treatment of frozen soil water. The northern part of the grid is covered with snow, a meter or more in some areas. The area of snow corresponds to areas where significant amounts of the soil water is frozen. Total soil moisture suggests nearly saturated conditions in the frozen-soil areas, and subsequently significant amounts of runoff in the area as snow may melt (e.g. around the periphery of the snow-covered area).

## Slide 8: Recent applications
Spring/Summer ARW-WRF experiments at NCAR/MMM
2005062100
Soil Moisture 0 – 10 cm
Soil Temperature 10 – 40 cm
Notes: HRLDAS has also been used to initialize some real-time forecast tests with ARW-WRF at NCAR/MMM. These were on a 4-km grid over most of the U.S. Mukul Tewari has put in a lot of work setting up HRLDAS and keeping HRLDAS going for this setup.
On the left is a soil moisture field from HRLDAS (my apologies for no scale, but the purple to blue to green to red is dry to wet). This field also illustrates one of the limitations of our data. The Stage IV precipitation analysis cuts off in just outside the boundaries of the United States, and the edge of the data can be clearly seen north of the Great Lakes, where we switch from using the Stage IV analysis to the Eta precipitation forecasts to drive HRLDAS.
On the right is a soil temperature field. You can clearly see the urban areas by their temperature signatures, a result of recent updates to the treatment of urban areas.

## Slide 9
Comparison of water equivalent snow depth
SNOW Analysis (NOHRSC)
MM5 model 2005-03-17 05:00 UTC cycle
HRLDAS 2005-03-17 00:00 UTC cycle
Notes: Comparison of water equivalent snow depth for MM5 forecasts restarted on March 17, 2005, 05Z (from a cold start on March 15, 12Z) versus SWE from the off-line HRLDAS run initialized on 03-17 00Z.
On the left NOHRSC snow analysis valid at approx that time. (05Z).
NOHRSC - The National Operational Hydrologic Remote Sensing Center (NOHRSC) provides remotely-sensed and modeled hydrology products for the coterminous U.S. and Alaska for the protection of life and property and the enhancement of the national economy. (from their web page)

## Slide 10: Recent and upcoming development
Surface emissivity
  Now a function of vegetation category
Urban modifications
Water routing scheme
Notes: Now, I’ll discuss a few recent developments and enhancements currently under development.
- Surface emissivity is now a function of vegetation category.
Other modifications I’ll describe in a little more detail are some modifications for urban environments, and a water routing scheme.

## Slide 11: Urban effects
Increased roughness length
  Drag due to buildings
Reduced surface albedo
  SW radiation trapping in urban canyons
Increased volumetric heat capacity of surface
  Concrete and asphalt roofs, walls, and roads
Increased soil thermal conductivity
  Storage of heat in and beneath urban surfaces
Reduced green vegetation fraction
10-40 cm T
2005062100
Notes: Mukul Tewari has introduced some modifications to Noah LSM to better account for urban effects. These modifications are:
- Increasing the roughness length
- Reducing surface albedo
- Increasing volumetric heat capacity
- Increasing soil thermal conductivity
- Reducing green vegetation fraction.
With these relatively simple modifications, the urban heat island effect is more effectively represented

## Slide 12
Water Routing
Lateral transport of surface and subsurface water from one grid cell to another
  E.g. flow of ground water from higher to lower elevations
Important for areas of complex terrain
Important for high resolution
O(1-km) or smaller
Important for long simulations
Notes: Dave Gochis of NCAR has been testing a water routing scheme in the Noah LSM. This is essentially the flow of ground and surface water down slopes from higher elevations to lower elevations, ultimately to streams and rivers where it is lost from the soil.
This tends to be a small effect, but it can become significant for areas of complex terrain, for high-resolution grids, and for long simulations. It’s these last two considerations (high resolution grids, and long-term simulations) that make the water routing of particular interest for HRLDAS.

## Slide 13
Detail of difference in total
evaporation (shaded) with and
without dual
routing shows terrain influence for
the 5 month period (1 Jan-1 Jun,
2001)
Broad decreases of 0-30 mm
evident over most high topography
Flat areas and topographic
convergence zones within high
terrain show modest increases
Many, though not all, steep slopes
show stronger decreases
Southern and eastern peripheries
show sizable localized increases
Aggregation/disaggregation
to/from 1km subgrid likely alters
location of routing influence
Contours are topography
Water Routing
Notes: This figure shows the effect of routing over for a 5-month HRLDAS simulation. Shaded is the difference in total evaporation between HRLDAS runs over the Colorado Rockies with and without routing.
Most of the high areas show a loss of evaporation as water is routed to lower elevations. Some areas, which appear to be associated with steep slopes, show greater decreases (representing a loss of water from the mountains), and some areas around the edges of the mountainous regions show large increases.

## Slide 14: HRLDAS Spin-Up
  One key issue:
  How long does it take for HRLDAS to reach its equilibrium or quasi-equilibrium state?
  Previous investigations mostly focused on the spin-up from random initial soil conditions or extremes
Notes: A natural but a key questions is: how long …
Previous studies by other groups are mostly interested in the spin-up of a land surface model from random soil conditions. What we are interested in, however, is the spin-up of this system if it is initialized by a land data such as NCEP Eta model which already reflect, to some degree, the recent history of precipitation. So we expect the spin-up from such conditions would be shorter.
For instance, if we want to start the forecast or a retrospective case study for 1 June 2002. How far do we need to go back to run HRLDAS to produce equilibrium soil conditions? In our spin-up numerical experiment. We assume 18-month lead time is sufficient, then we tried to run it with various lead time and see how different the soil moisture and temperature would be on 1 June 2002 if we started HRLDAS in Feb 2001 or we started HRLDAS in May 2002.

## Slide 15: HRLDAS Spin-Up
1st layer soil moisture
Volumetric soil moisture
RMS difference (m3m-3)
Coarse
soil
Medium
soil
Fine
soil
3rd layer soil moisture
< 0.02
0.02 <
< 0.1
0.1 <
Quick spin-up for coarse soil texture
Notes: This plots shows the RMS difference of soil moisture between runs with different lead time as compared to the 18-month lead-time run. Left is 1st layer and right is 3rd layer soil moisture. The green blocks representing RMS smaller than 0.02, red between 0.02 and 0.1, and blue is more than 0.1
The soil texture found in the HRLDAS domain can be roughly divided into coarse, medium and fine soil. It is clear that the 1st layer soil spin up faster than deep layer. In fact, after one month, except for a few category, the difference is very close to 0. The spin-up is fast for coarse soil texture like sand, most soil texture would need about 12 month spinup.

## Slide 16: HRLDAS Spin-up
1st layer soil temperature
< 0.5
0.5 <
<1.0
1.0 <
Soil temperature
RMS difference (K)
Coarse
soil
Medium
soil
Fine
soil
3rd layer soil temperature
Quick spin-up for medium soil texture
Notes: This is the same type of plots as previous one but for soil temperature. Green is RMS less than o.5 degree, blue is more than 1 degree, red in between.
Again, 1st layer soil reaches equilibrium state quicker than deep layer and most soil texture will take 12 month to have RMS less than o.5 degree.
But note that unlike soil moisture, fine soil texture has shorter spin-up time than coarse soil. This is not totally unexpected, because Fine soil texture facilitates water movement, but fine soil has larger thermal conductivity.
What would this mean to a coupled NWP model?
Although the final product of HRLDAS are soil moisture and temperature, the final goal is to provide accurate surface heat fluxes as lower boundary conditions to coupled forecast model.

## Slide 17: HRLDAS Spin-Up
Sensible heat flux
Latent heat flux
< 5
5 <
< 10
10 <
Surface heat flux
RMS difference (Wm-2)
Coarse
soil
Medium
soil
Fine
soil
Soil temperature has more
Impact on surface heat flux
Notes: The surface heat flux is integration of soil moisture and temperature evolution. It appears that soil temperature has more impact on surface heat fluxes. You can see the fine soil texture has quicker spin up.

## Slide 18: Plans
Plug-compatibility between Noah physics code in ARW-WRF and HRLDAS
Offer HRLDAS for community use
Support code in the context of ARW-WRF
Sample shell scripts and programs
Notes: And finally, some plans on where we hope to take HRLDAS.
One goal is to have a Noah LSM code that is plug-compatible between ARW-WRF and HRLDAS. This will allow advances in one realm to be immediately applicable to the other. It also allows us to insure that we’re using the same physics for HRLDAS as for WRF.
We hope to be able to offer HRLDAS for community use, and hope to be able to support the code in the context of ARW-WRF
Since data collection and organization tends to be the most difficult aspect of HRLDAS, we hope to offer some sample shell scripts and programs as an example for users as a way to handle this task.